Town of Derry, New Hampshire

REQUEST FOR PROPOSALS			B21-120

July 31, 2021

The Town of Derry, New Hampshire seeks proposals for:

Aluminum Two Axle Open Top Walking Floor Trailer

Offered by:

Department of Public Works

RFP Process Coordinated by:

Michael A. Fowler, DPW Director

(603) 432-6144

The Town of Derry is accepting quotes for furnishing:

One new 116 – 120 cy open top aluminum walking floor trailer

The trailer furnished shall meet the following minimum specifications:

116-120 cubic yard capacity – aluminum open top

Aluminum Body and Frame

48 feet length – 102 inch width – rear axle dump – front axle lift

8’ 2” spread axle

Air ride suspension

Sides – 100” - 3/16” Aluminum

Top Rail – 6” x 4” x 3/16” or larger

(4) Aluminum wheels outside and (4) painted rims inside with 22.5” tires.

Tailgate – Barndoor Type hinged on curbside

Chassis – 10” I-Beam rear to landing gear

Axles – 5” round 25,000 lb Axles (two axles, not three)

Kingpin – 36” on 3/8” pin plate

Substructure – cross members 12” on center

Landing Gear – Holland Mark V or equal on driver’s side

Floor – Keith Hallco or equal

Hook Holder for Hydraulic hoses

Bumper – ICC Pusher Bumper with 2 tow hooks

Delivery to Derry, NH– To be included in price quote

The specifications shall include all items required to comply with USDOT/FMSCA regulations. Vendor shall furnish full specification sheet with quote.

Questions may be directed to the Derry Transfer Station Division (603) 432-4650.

Sealed Quotes are to be forwarded to:

Michael A. Fowler, P.E.

Director, Derry Municipal Center

14 Manning Street

Derry, New Hampshire 03038

SEALED Proposals will be accepted until 4:00 p.m. on Friday, August 27, 2021. Proposals received after this time will be returned unopened. Faxed proposals will not be accepted.

The Town of Derry reserves the right to reject all bids for any reason.

Given the current supply chain challenges, there will be no defined delivery date. However, each proposer shall identify a delivery date for consideration as part of the bid award process.